1. After the filtering, segmentation --> the point cloud of the top surface is extracted. This point cloud data is the input of the system
2. Load the point cloud data
3. voxel grid downsampling --> to reduce the number of points
4. calculate mean Z value of the points (mean height)
5. Create a 2D reference plane, whose height is equal to the mean Z value of the point cloud of the top surface
6. remove the points below the reference plane, and retain the points above the reference plane
7. Remaining point clouds are projected onto the 2D reference plane
8. Convert all the point into 2D points (remove the Z coordinate information) --> point_extracted
9. Apply DBSCAN algorithm to automatically cluster the points into groups according to their density.
*The DBSCAN algorithm is performed using scikit-learn python library, details of the method showed in the ipython html file.
9.1 --> create an open3D object here
pcd_2D = o3d.geometry.PointCloud()
pcd_2D.points = o3d.utility.Vector3dVector(point_extracted)

9.2 convert the open3D points to numpy array for further processing
extracted_2D_downsampled = np.asarray(downsample_pcd_2D.points)
10. Get the contour of each point cloud clusters
alpha shape (concave hull) algorithm is used to calculate the contour
the method was learned from online
tuning the parameter for concave hull fitting: alph, current value of alpha for fitting: 5 (default)

Add the bounding box to the whole graph, the bounding box is the target cross-section of the manufactured part
Another method for concave hull polygon fitting algoithm (the one we actually use)
http://www.rotefabrik.free.fr/concave_hull/
This program uses shapely instead of numpy or open 3D
---> this algorithm can be explained in detail!
Return:　－＞ the bounding point of the polygon，　and the polygon

11. Python “Inpolygon” function
- It allows the input polygon vertices to describe multiple NaN-delimited polygons.
- The polygons can also include holes.
- returns true/ false to tell if the points are lie in the polygon

Method we use: python shapely library

polygon = Polygon(boundary_points)
# boundary of the polygon = LinearRing
linearring = LinearRing(list(polygon.exterior.coords))

print (polygon.contains(linearring))
print (polygon.touches(linearring)) --- if on the boundary of the polygon

--------- In our case: Plot the polygon with clustered bulge area as holes

12. Check points inside or outside the polygons

13. determine the line and polygon intersection point
14. sorts the rows of intPoints in ascending order based on the elements in the first column

15. Line in polygon segmentation function

16. the grid line creation function

17. the zig-zag line segmentation function

Input
        - line_elements: a list object, contains a list of created grid lines (each element is a LineString object)

    Output:
        - segment_inside_collection: a list object, each element is a MultiLineString object containing the inside polygon portion of line
        - segment_outside_collection: a list, each element is a MultiLineStirng object containing outside portion of the line
- intersection_points_collection: list, each element is a MultiPoint object containing the intersection point of linea and polygon

17. combination – final result